## Slide 1: Key Parameters for Credit Appraisal
Appropriate DSCR
Use of P90 or other Probability Level for Debt Sizing
Establishment of Downside Case
Cash Sweeps for Commodity Prices
Contract Off-taker and Diagram
Tenure and Maintenance Reserves

## Slide 2: Presentation on Green and Blue Hydrogen

## Slide 3: Reprehensible Hydrogen Skeptics

## Slide 4: Subjects Addressed
Overview of Green and Blue Hydrogen
Locational factors requirements
Demand for Green/Blue Hydrogen & their feasibility
Life Span and Ongoing Capex Requirements
Due Diligence Requirements for Lending
Key Parameters for Credit Appraisal

## Slide 5: Overview of Green and Blue Hydrogen
Chemistry and Uses of Hydrogen
Cost Structure and Efficiency (China versus Siemens)
Emissions of Blue Hydrogen versus Grey Hydrogen
Challenges of Green Hydrogen

## Slide 6: Part 1: Overview of Green and Blue Hydrogen – Chemistry and Uses

## Slide 7: Potential and Current Hydrogen Uses

## Slide 8: Hydrogen Colours

## Slide 9: Hydrogen Chemistry
The most common method of making hydrogen today is steam methane reformation (SMR). The process combines methane (from natural gas) and water at very high temperatures (about 900°C) to produce a mix of carbon monoxide, carbon dioxide (CO2) and hydrogen.
For SMR grey, the reaction is represented by this equilibrium:
        CH4 + H2O ⇌ CO + 3 H2.
Electrolysis is the green alternative:
Alkaline electrolysis and Proton Exchange Membrane are established technologies.
Fuel Cells for Transport and Electricity Storage
Fuel Cells Use Hydrogen as an input and produce
Fuel cell and electrolysis is not a new topic. Invented by William Grove in 1839
2014 Commercialized fuel cell vehicle by Toyota

## Slide 10: Steam Methane Reforming – Grey (Bad) Hydrogen
Use Natural Gas
CO2 Must be Produced
In Refinery or Steel Plant
Less Downstream

## Slide 11: Green Hydrogen from Electrolysis
Converting water into hydrogen has been around for a long time
Need stack which is coated with platinum and depends on the platinum price
Until recently, smallest SMR is bigger than largest electrolyzer
You can make the electrolyzes modular
Question about economies of scale
Efficiency is 60% for both electrolysis and for the fuel cell.
Efficiency = output/Input
Output is 33.33 kWh/kg
60% = 55.55 kWh/kg

## Slide 12: Illustration of Ingleside Proposed Blue Hydrogen/Ammonia
Choose the picture according to your opinions about CCS

## Slide 13: Very Little Green versus Grey Hydrogen - .1% of Ammonia

## Slide 14: Green Hydrogen - Electrolysis from Proton Membrane
Illustration of Electrolysis
Stack
Key Modelling and Economic Issue – Stack has a life that is different than the other equipment
Platinum

## Slide 15: Alkaline and Proton Membrane

## Slide 16: Operation of Fuel Cell – Reverse of Electrolysis
Hydrogen is input and produces electric current. No Carbon Produced
Same as issue with the life of the stack – like the life of a battery that depends on the number of cycles

## Slide 17: Part 1b: Overview of Green and Blue Hydrogen – Cost Structure and Efficiency

## Slide 18: Efficiency and Capacity Factor
Question: What is the difference between efficiency and capacity factor
Banks and Investors: Concern with the overall cost

## Slide 19: Why Are We Even Discussing Green Hydrogen 1 - German Solar Feed-In Tariffs and Managing Risk
Example of government policy that worked. Idea to make very simple tariff to finance projects and then achieve scale.

## Slide 20: Why Are We Even Discussing Hydrogen 2 - Module Prices and Polysilicon

## Slide 21: Important to Understand Basic Energy Conversions – kWh/kg = 33.33 as Hydrogen Output

## Slide 22: IEA, Benchmarks and Economics
Convert kWe to kWh2 using 33.33 kWh/kg energy conversion
Electrolyzer based on kWe using efficiency reduction
Blue and grey hydrogen based on kWh2
Largest uncertainty on cost is from Electrolyzer

## Slide 23: Some Basics of Efficiency Conversions Multiply kWh/kg by USD/kWh or MMBTU/kg by USD/MMBTU
Energy Content of H2 in kWh 33.33 kWh/kg
Conversion from kwh to BTU 3,412 BTU/kWh
Energy Content of H2 in BTU 113,721 BTU/kg
IEA Data
  Electrolyzer Efficiency – 64%
  SMR Grey Efficiency per IEA – 76%
  SMR Blue Efficiency per IEA – 69%
Need Ratios to Output – kWh/kg or MMBTU/kg
Need these because fuel is USD/kWh or USD/MMBTU
Electrolyzer  33.33/.64 = 52.07 kWh/kg
SMR Grey  .113721/.76 = .1496 MMBTU/kg
SMR Blue  .113721/.69 = .1648 MMBTU/kg

## Slide 24: Estimate of Capital Expenditures – No Economies of Scale
SOEC is Solid Oxide
Note the cost of USD 650/kW with a very wide range in the efficiency
Note also that ALK dominates in terms of cost and efficiency

## Slide 25: Chinese Electrolyzer Cost Dramatic Cost Reduction – Price of USD 200/kW to USD 205/kW

## Slide 26: PEM versus Alkaline – Can you Turn off Alkaline at Night when the Sun is Not Shining and there is No Wind
It is often noted that PEM electrolysis has a fast response ramp-up and ramp-down capability, as well as a wide dynamic operating range of 0-100% – making it ideal for generating hydrogen using excess renewable energy.
One of the advantages of [atmospheric] alkaline is that it’s a proven technology, it’s been around... for 100 years or so. It’s a technology that is well known. It is probably around half the price of PEM [to buy],”
In any given 24-hour period, there will often be one or two hours where the electrolyser has to be turned off, and on a windless night it could be up to 12 hours. “And that’s a challenge for alkaline of particular importance is the ability to start things up from a cold start very quickly.”
Alkaline electrolyzers can take up to 50 minutes to get up to full operating speed, compared to less than five minutes for PEM.

## Slide 27: Part 1c: Overview of Green and Blue Hydrogen – Emissions from Green, Blue and Grey versus Battery and Petrol

## Slide 28: Emissions of Electricity Generation (IEA)
Include in the operating cost
Use a cost of USD/Tonne that can range
The IEA uses USD 30/Tonne
In Europe the cost is higher
Convert GWH to Tonnes using some table

## Slide 29: How Much Natural Gas and Emissions to a km using SMR – Grey or Blue
Get from efficiency of electrolyzer, efficiency of car, efficiency of electricity and efficiency of battery
.16 MMBTU/kg .008 kg/1 km .00128 MMBTU/km
Heat Rate 7,000 BTU/kWh .188 kWh/km 80% Efficiency .001316 MMBTU/km
More natural gas used for electric car.
If avoid 90% of emissions from natural gas are reduced, the emissions are much less.
Natural gas use is 12,800 per BTU versus
13,160

## Slide 30: Computed Emissions from Hydrogen (FC BEV) and Battery Cars (BEV)
Note the dramatic effect of Methane Leaks

## Slide 31: Emissions from Natural Gas Leaks

## Slide 32: Part 1d: Overview of Green and Blue Hydrogen – Hydrogen Challenges

## Slide 33: Hydrogen CCS Adding Cost of Leakage of Natural Gas
The IEA estimates the cost of abating 70% methane leaks would range from $6/MMBTU to $30/MMBTU.
The authors then moved their attention to CCS and instead of finding 90% capture, they calculated an overall capture rate of 52%.
Shell says 90%

## Slide 34: Green Hydrogen Efficiency Problem - Electricity to a KM Using Electrolysis and Battery
50 kWh/kg .8 kg/100 km 40 kWh/100 km; .40 kWh/km
Efficiency 80% .15 kWh/km .188 kWh/km

## Slide 35: Problem of Green Hydrogen – Proven Technology
Parameters that cannot now be guaranteed with a contract
  Efficiency
  Degradation
  Cost of Replacing the Stack
  Time period for Replacing the Stack
Other Problems
  As a very small molecule, Hydrogen can easily escape
  Hydrogen is so light and need to store a lot to get energy
  Hydrogen filling and delivery
  Hydrogen infrastructure for transport
  Escaped Hydrogen can aggravate greenhouse gas when combines with other gasses

## Slide 36: Part 2: Location of Green and Blue Hydrogen

## Slide 37: Location of Green and Blue Hydrogen
Need for Wind and Solar Combined
Irradiation Levels and Levelised Cost of Electricity for Green Energy
Selected Other Locations and Characteristics
Yield and Price of Electricity
Importance of Capacity Factor of Green Hydrogen
Sea Ports and Proximity to Markets
Conversion to Ammonia and Current Transport
Markets for Green Ammonia
Correlation with Natural Gas

## Slide 38: The Dream – Future – No Electricity or Hydrogen Distribution or Downstream
Electricity and Hydrogen Production
No Distribution Cost
No T&D cost for electricity
Limited Storage Needs
Spread out dispensing

## Slide 39: Alternative Renewable
Blue Hydrogen depends on natural gas that is not already exported with LNG
Immediately divide 5,800/8760 to get 66%

## Slide 40: Bloomberg Forecast of Green Hydrogen Price/kg

## Slide 41: Solar - 1
Nothing that special, but good

## Slide 42: Solar - 2
Maybe 31% with tracking and bi-facial

## Slide 43: Wind

## Slide 44: Required Price
Note the change in the required price with the capacity factor.
This is dramatically aggravated with higher capital costs.

## Slide 45: Illustration of Economics and Planned Projects

## Slide 46: H2 Transport and Location

## Slide 47: Location and Blue Hydrogen
Depends on Natural Gas Reserves and Finding a place to store the CO2

## Slide 48: Part 3: Demand for Green/Blue Hydrogen and Feasibility

## Slide 49: Demand for Green/Blue Hydrogen and Feasibility
Alternative Uses of Hydrogen
Derivation of Demand from Emission Prices in Europe and U.S.
Levelised Cost and Drivers of Green versus Blue Hydrogen
Storage of Hydrogen versus Storage of Electricity

## Slide 50: Hydrogen Demand – Ammonia and Refining
IEA

## Slide 51: Ammonia
A big use of Hydrogen is Making Ammonia for Fertilizer

## Slide 52: Levelized Cost of Green Ammonia

## Slide 53: Storage Case 1 – Does Not Make Sense

## Slide 54: Storage Case 2: Need Hydrogen and Better to Store Hydrogen in Cask than Electricity in Lithium

## Slide 55: Part 4: Life Span and Capital Expenditure Requirements

## Slide 56: Life Span and Capital Expenditure Requirements
Stack Life and Hours of Use
Degradation in Electricity Supply and Projected Balance of System
Prediction of Future Capital Expenditures and Price of Platinum
Guarantees from EPC or Suppliers
Operating Expense of Green versus Grey and Blue
Sources of Real Information and Financial Models

## Slide 57: Credit Issues with Blue Hydrogen
Can we find places to store the hydrogen
Does the equipment really capture 90% of the hydrogen
What is the true efficiency of the CCS equipment
The technology is certainly non-proven

## Slide 58: Example of Replacement and Degradation

## Slide 59: Example of Degradation

## Slide 60: Stack Life in Hours
Total Hours from 60,000 to 100,000
If the capacity factor is 25% and there are 100,000 hours, the life is 100,000/(8760*25%)

## Slide 61: Measuring Risk with Project Finance and DSCR

## Slide 62: Debt Terms Example

## Slide 63: Response to Hydrogen Skeptics

## Slide 64: Levelised Cost of Energy with Battery
Measure Capital Cost with Storage
Add Costs with different lives
Create simple example

## Slide 65: Duck Curve, Camel Curve and Malaysia Flat Loads

## Slide 66: Wind Variation and Zero Prices